DisasterRadio
A low-bandwidth wireless mesh

---
WiFi mesh networks
- Pros
  - High bandwidth
  - IP transport
- Cons
  - Short range or
  - Require directional antennas, rooftop mounting, runnning cable
    - Most nodes are short range

---
How do we solve rooftop mounting?

---
Solutions?
- Running cables is problematic
  - Run all nodes on solar + battery so they won't need power
  - Relay to separete router inside of building
- Mounting and aiming is problematic
  - Remotely aimable antennas?
    - Phased array? Many directional antennas + antenna switcher?
  - Use drones to lift node onto roof?
    - How do we prevent them from blowing away in strong winds?
      - Weigh them down with water? Self-filling rain water container? Only deploy during strong rains?

---
Minimal useful implementation?

---
Minimal useful implementation
- Entirely solar powered
- No cables
- No mounting
- No aiming
- Some amount of bandwidth
- At least one useful application
  - Chat? Microblogging?

---
DisasterRadio node version 0

---
DisasterRadio node version 0

---
Low-bandwidth FSK/CSS radios
- Pros
  - Long range, even without directional antennas
  - Very low power
  - Cheap
- Cons
  - Very low bandwidth
  - Very small packet size (usually smaller than min IPv6 packet)
  - Not suitable as IP transport
  - (usually) no built-in channel sharing mechanism (no TDMA, CSMA, etc)
    - Low frequency utilization
- Antenna: High gain „omni“-directional (flattened donut radiatation pattern)

---
0.041 W
0.373 W
RN2903 is LoRaWAN but layer 2 can be disabled

---
Stated range (RN2903)
- > 15 km in suburban settings
- > 2 km in dense urban environements
  - https://www.digikey.com/en/articles/techzone/2016/nov/lorawan-part-1-15-km-wireless-10-year-battery-life-iot
- > 3 miles (4.8 km) in urban environments
  - Microchip (manufacturer)
- Easy to cover large areas!

---
Processor and WiFi
- ESP8266 / ESP32
  - Low cost
  - Large community
  - Integrated WiFi
- Downward-pointing high gain panel
  - Cheap (on-PCB design possible)
  - Suitable directionality for covering inside of house/apartment

---
Solar + battery
- Solar
  - 3-4 watt
  - 5-6 volt
- Battery
  - Single 18650 li-ion cell
- Needs MPPT solar charge and battery controller
  - 10% to 90% charging to increase battery lifetime
  - Temperature monitoring
  - Elektra's design modified for low power?
  - AdaFruit's design: https://www.adafruit.com/product/390

---
First prototype
- 100% off-the-shelf components
  - Minimal soldering
  - Inefficient
  - Short life
  - Possibly unsafe

---
What can it do?
- Probably no IP
  - Tiny packets can't do IPv6
  - Small amount of total network bandwidth: Easy to saturate network
- Small twitter-sized sized messages
  - ~160 bytes (after header, checksum, signature)
- Apps
  - Chat and microbloggin
  - Community mapping (like Tidepools) with local vector maps

---
Software
- Using NodeMCU (lua) for rapid prototyping
  - Issues with memory leaks
  - Not yet ready for ESP32
- Integrated
  - DHCP server
  - DNS server
  - Web server
    - Serving up chat app
  - Telnet lua console for development

---
Meshing
- v0
  - Flooding only: Every node gets every message
  - Off-the-shelf components
- v1
  - Nodes subscribe to feeds and publish messages to feeds
  - Custom PCB with on-board WiFi panel antenna

---
ToDo
- Hardware
  - Evaluate radio transceivers
    - RN2903
    - RFM95W
    - DRF1276G
  - Evaluate solar battery charge systems
  - Evaluate ESP32 as alternative
- Software
  - Fix memory leak issue
  - Add WebSocket support

---
Thank you